## Slide 1
DE1-SoC Real-Time Room EQ Correction — System Block Diagram
EXTERNAL HARDWARE
FPGA FABRIC (Cyclone V 5CSEMA5F31)
HPS (ARM Cortex-A9 @ 800 MHz)
Line-In Jack (J2)
3.5mm TRS
Mic-In Jack (J1) — unused
Wolfson WM8731 Audio CODEC (24-bit, 44.1 kHz)
Line-Out Jack (J3)
3.5mm TRS → Speakers
[ Speakers ]
50 MHz Clock (Si5350C on board)
① Audio PLL (Intel PLL IP) CLK_50→18.432 MHz
② I2C Controller (OpenCore I2C Master) WM8731 config
③ I2S Audio CODEC Interface Deserialise ADC Serialise DAC (AUD_BCLK / LRCLK / DATA)
⑤ Input Sample FIFO (Altera SCFIFO) 512×24-bit
Mode MUX (EQ path ↔ CAL path)
⑫ ADC DMA FIFO (CAL RX buffer) 512×24-bit
⑪ DAC DMA FIFO (CAL TX buffer) 512×24-bit
⑥ FIR Filter Core (Altera FIR II IP) 1024 taps, 24-bit DSP block–packed 48-bit accumulator
⑦ Overlap-Add Buffer (M10K On-Chip RAM) 1023×24-bit tail store
⑧ Coefficient RAM (M10K Dual-Port) 1024×32-bit Port A: HPS write Port B: FIR read
⑨ Output Sample FIFO (Altera SCFIFO) 512×24-bit
⑬a DMA Controller (TX – sweep out) DDR3→DAC DMA FIFO
⑬b DMA Controller (RX – room record) ADC DMA FIFO→DDR3
⑩ Control/Status Register Block MODE, COEFF_LOADED OVERFLOW, GAIN
⑪ HPS→FPGA Lightweight Bridge (Avalon-MM 32-bit)
FPGA→HPS Bridge (Avalon-ST DMA stream to HPS)
64 MB SDRAM (FPGA-side, optional scratch)
⑫ HPS (ARM Cortex-A9) Calibration SW: • Sweep generation • sd.playrec() equiv. via DMA • Room IR estimation (FFT deconvolution) • FIR coeff derivation (regularised Wiener) • Write coeffs to Coeff RAM via bridge • Set MODE = EQ
DDR3 SDRAM (1 GB) Sweep buf, Recording buf FFT workspace, Coefficients
Linux (Angstrom / Yocto) or Bare-Metal C app
I2S ADC
I2S DAC
I2C
18.432 MHz (AUD_XCK)
CLOCK_50 50 MHz
← ADC samples (CAL mode, orange dashed)
← Sweep samples (CAL mode, orange dashed)
LEGEND
────── Real-time EQ audio path (blue arrows)
- - - - Calibration DMA path (orange dashed arrows)
────── Control / config (dark arrows)
────── Clock distribution (purple arrows)
Numbered boxes ① – ⑬ correspond to submodule list in design doc
OPERATING MODES
CAL MODE: HPS streams sweep via DMA TX → WM8731 DAC → Speaker Room response → WM8731 ADC → DMA RX → HPS DDR3 HPS computes room IR + FIR coefficients, writes to Coeff RAM
EQ MODE: Line-In → WM8731 ADC → I2S → Input FIFO → FIR Core → Overlap-Add → Output FIFO → I2S → WM8731 DAC → Line-Out